## Slide 1: Modelling energy use in buildings: making it simpler
Buildings Under UNFCCC Flexible Mechanisms 14th March 2011, Bonn, Germany
Dr Rajat Gupta, Consultant UNEP-SBCI
rgupta@brookes.ac.uk
Credibility
Notes: <number>
<number>
This presentation has to be delivered in 10 minutes
Ladies and Gentlemen
It is a great pleasure for me to be there today and to have the opportunity to present the first ever common carbon metrics, providing a basic building block for any international policies to reduce greenhouse gas emissions from buildings.
The Common Carbon Metric protocol and reporting template provides industry with a globally consistent methodology by which to measure energy use and report related greenhouse gas emissions from building operations.
This Common Carbon Metrics has been jointly developed by a large number of national and international organizations and experts concerned with energy efficiency and climate mitigation in the building sector.
In this presentation I will give you a brief introduction to the Metrics, and I will outline how it may enable the building sector to contribute significantly through emission reductions to a low-carbon society.

## Slide 2
“in theory, theory and practice are the same, in practice they aren’t”
SANTA FE INSTITUTE for research into complex systems
Notes: <number>

## Slide 3
Background
  The Big picture
  Role of building energy models: predicting energy use
  Ways of assessing energy use in buildings
Building energy prediction: limitations and complications
  The Credibility Gap
  Understanding the full picture: impact of occupant behaviour
Changing role of building energy models
  Modelling energy use of a large number of buildings rapidly
  Ethical reporting: avoiding ‘green wash’ and ‘eco-bling’
Conclusions and final thoughts
  Where next…
Structure of this presentation
Notes: <number>

## Slide 4
Background
Notes: <number>
<number>

## Slide 5
People
Buildings
Climate
Culture and preferences are partly determined by climate
People control buildings to suit themselves in climatic context
Building ameliorates climate to suit occupants within cultural norms
Energy use is influenced by climatic, social, economic and cultural context
Dynamic three-way interaction between climate, people and buildings dictates our energy needs in buildings
(Source: Professor Fergus Nicol, 2008)
The Big Picture

## Slide 6
Baselining: Assessing energy and CO2 emissions from all energy-related end-uses in buildings, by:
  Building energy modelling (predicting energy use) – examples are Ecotect, IES, TAS, Energy Plus, ESPr, DOE
  Actual energy measurement (metered energy data)
Benchmarking existing performance against best-practice, peers
Target setting: establishing ambitious CO2 reduction targets – Relative (60%, 80%) or Absolute (15kgCO2/m2/year)
Evaluation and appraisal of low-energy and low-carbon measures and technologies to achieve targets. (Building energy modelling)
Implementation of actions
Monitoring, reporting and verifying the energy and CO2 reductions achieved as a result: sharing experiences. (Actual energy measurement)
Monetisation of savings: future carbon markets & emissions trading for buildings.
Role of building energy modelling: predicting energy use

## Slide 7
Predictive energy simulation models
  Computer programs which are used to generate an energy performance prediction from calculations.
  IES, TAS, Energy Plus, ESPr, eQuest
2. Simplified energy models or Correlation tools
  Measure a particular element such as energy efficiency or thermal comfort and focus on providing a quick evaluation of a proposed design in the form of a simple indicator, such as UK’s Standard Assessment Procedure (SAP) for dwellings
Scorecard rating tools
  Award points against pre-defined set of criteria which are then weighted and an overall rating is given, such as LEED (US), BREEAM (UK), Griha (India)
Actual energy consumption measurement
  Actual data is measured by fuel (gas, electricity etc) consumption or by end use (heating, cooling, appliances) if buildings are specifically sub-metered.
Approaches for assessing energy use in buildings
Notes: <number>

## Slide 8
Building energy predictions: Limitations and complications
Notes: <number>
<number>

## Slide 9
The Credibility Gap: Prediction and Actual
(Source: Bill Bordass, 2005)
Notes: <number>

## Slide 10
The Credibility Gap: Prediction and Actual
Notes: <number>
<number>

## Slide 11
Modelled and actual energy use: Credibility gaps
Bills | Total consumption (kWh) | Cost (£) | Per unit area (kWh/m2)
Gas (29 Jan 08-28 Jan 09) | 9465.16 | 336.05 | 123.08
Electricity (Lighting + fans/ pumps + appliances) | 2481.00 | 354.15 | 32.26
Water use | - | 200.85 | -
Total (energy only) | 11946.14 | 690.2 | 155.35
SAP Energy model | Total consumption (kWh) | Cost (£) | Per unit area (kWh/m2)
Gas | 24,797.14 | 404.19 | 322.42
Electricity (Lighting +fans/ pumps) | 802.52 | 57.14 | 10.44
Total energy | 25599.66 | 461.33 | 332.86
1930s Victorian terrace house in Oxford, UK
Notes: <number>

## Slide 12
Unregulated Energy Use includes: plugload, server rooms, security, external lighting, lifts etc.
Special Functions include: trading floors, server rooms, cafeteria etc.
Extra occupancy
& operating hours
Actual – Real energy use
Special
functions
Model forecast
Forecast Regulated CO
Part L
2
Unregulated CO2
Inefficiencies
From BMS
Regulated Energy Use includes: fixed building services, heating, hot water, cooling, ventilation, lighting
Energy use in buildings: the full picture
(Source: Aedas Architects, 2010)
Notes: <number>
Energy use - the full picture
Recent research into operational energy use points to a worrying discrepancy between forecast and actual energy use.
This diagram describes the key contributors to this discrepancy, namely that during design stages the legislative requirements for energy forecasting relates to fixed building services only. However occupant-related energy consumption can account for over 2/3rds of a building's total energy use. Reducing this requires input from clients, consultants, contractors, facilities managers and occupants. CarbonBuzz campaigns for better awareness of these factors amongst all stakeholders.

## Slide 13
The theoretical potential of the base building’s fabric and services under standard assumptions is considered.
However the following are NOT considered:
The build quality and commissioning of the above.
The fit out by the occupant.
The equipment added by the occupant.
The pattern of use of the building & equipment.
Operation, control, maintenance, management of all the above, by both landlord and tenant.
So, what do energy models consider and ignore?
(Source: Bill Bordass, 2005)
Influenced by socio-economic-cultural factors
Notes: <number>
<number>

## Slide 14
(Source: Energy for Sustainable Development, 2007)
Assessing energy use in buildings: Approach in UK
Notes: <number>

## Slide 15
Changing role of building energy models
Notes: <number>
<number>

## Slide 16
GIS Map-based domestic carbon-counting and carbon-reduction model Bottom-up toolkit to measure, model, map and manage energy use and CO2 emissions, on a house-by-house level.
Assessing energy use of a large number of buildings rapidly
(Source: www.decorum-model.org.uk)
Carbon mapping of houses in North Oxford : DECoRuM

## Slide 17
1. Building energy consumption or energy imported (CO2 produced)
2. On-site renewables (CO2 saved)
So poor buildings can’t hide under low-carbon supplies (avoids Greenwash, Eco-bling!)
Reporting energy and carbon performance ethically

## Slide 18
‘Real’ utilisation factors (Refer to energy use of comparable existing building types)
‘Bespoke’ occupancy schedules for different building typologies (empirical studies on building energy consumption essential, CCM type methods could help)
Ongoing monitoring and evaluation to understand what really happens in use (rapidly feed back this information into models)
Transparency and accountability is essential to avoid unintended consequences (Validation of model predictions with actual utility data)
Avoid unmanageable complication (Keep things as simple as possible)
Towards evidence-based assumptions in energy models
Notes: <number>

## Slide 19
Conclusions and final thoughts
Notes: <number>
<number>

## Slide 20
Two different approaches to measuring and reporting energy use in a building exist:
TOP-DOWN
  Work down from annual fuel consumption
BOTTOM-UP
  Work up from the components of energy use
Ideally, reconcile between top-down and bottom-up, to connect inputs with outcomes
Where next?
Notes: <number>

## Slide 21
Define the boundary of the premises (building)
Collect annual energy use data by fuel
Identify the building type and floor area
Multiply each fuel use by the appropriate emission factor
Calculate performance indicators:
  kWh/m2 per annum.
  kgCO2e/m2 per annum.
Adjust if necessary, e.g. for weather and/or occupancy.
Review against appropriate reference data, e.g. published benchmarks, performance in previous years
Establish energy and CO2 reduction targets
Using a Common Carbon Metric based approach: making energy assessment simpler
Notes: <number>

## Slide 22
A dynamic three-way interaction exists between climate, people and buildings that dictates our energy needs in buildings – It is essential to consider this in building energy models and simulation.
Credibility gaps are increasing between energy predictions from models and actual energy consumption in buildings: Reliability is important
Energy use in buildings should be reported ethically: no ‘green wash’
Count ALL energy uses when developing energy models: applicability
Think of data availability and user expertise: avoid information overload
Making it simple – Common Carbon Metric based-approach using complementary top-down and bottom-up approaches.
So in conclusion….
Notes: <number>
<number>

## Slide 23
"We cannot solve our problems with the same thinking we used when we created them."
Albert Einstein
Its really about Re-Thinking …
Thank you for listening!