## Slide 1: SSC-NM0053
Determination of Greenhouse Gas Emissions Reductions Based on Whole-Building Simulation of Building Mitigation Efforts Using eQUEST/DOE-2.2
Anne Arquit Niederberger
March 14, 2011

## Slide 2: Motivation
Need to isolate effects of mitigation measures
No comprehensive methodology for buildings
Better guidance needed for use of building simulation under CDM
Why single building energy simulation framework?
  Make EB, not DOEs, responsible for approving credible model framework
  eQUEST/DOE-2.2 widely-used globally, free of charge, well-documented, approved by many regulatory regimes
  Increase consistency across project activities
  Facilitate capacity building by focusing resources
  Build publicly available catalog of calibrations to aid learning and analysis (reduce transaction costs)
Notes:   Project 1794 (AMS II.E.) used simulation modeling
  AMS III.AE. explicitly includes simulation modeling
<number>

## Slide 3: History
20 April 2010: Submitted by World Bank
15 June 2010: SSC WG26 Recommendation
16 August 2010: SSC WG27 Revised Recommendation
  SSC WG recommended that the Secretariat retain further expert input
  SSC WG will further consider the draft methodology upon receipt of such input
  SSC WG would welcome participating in, and perhaps even co-organizing, a buildings and building simulation workshop should the methodology’s sponsor care to organize such an event

## Slide 4: ELEMENTS OF THE METHODOLOGY

## Slide 5: Technology/Measure
GHG emissions mitigation from:
  On-site building energy supply
  Building energy end-use (thermal and/or electrical, including plug-loads)
Existing building retrofits and new construction
Type III (RE, EE, fossil fuel switch, passive design)

## Slide 6: Applicability
Applicability
eQUEST/DOE-2.2 building energy simulation package must be used
Project participants can demonstrate that building energy simulations (and related calibrations) will be performed by a skilled operator
Underlying PDD
Green Public Housing Project (Tianjin, China)
7 residential towers (569 apartments); floor area 37,885 m2
Measures
  On-site solar
  Building envelope
  Efficient building technologies, fixtures, lighting & appliances

## Slide 7: Additionality
Can be demonstrated through achievement of voluntary green building certification, if standard is more stringent than any local mandatory requirements
  Requirement to file F-CDM-Prior consideration waived
  Crediting period for such project activities may begin from the date of first occupancy (not prior to 1 January 2009)
Otherwise, SSC additionality provisions included in Attachment A to Appendix B of 4/CMP.1 Annex II
Notes: <number>

## Slide 8: Baseline
Baseline Scenario
Retrofit: Existing building in pre-retrofit condition
New construction: Planned building as it would have been constructed were it not for the CDM project activity:
  Existing building code or
  Typical of the building stock
Baseline Energy Consumption
Simulated

## Slide 9: EMISSIONS REDUCTIONS

## Slide 10: Step 1: Data Collection
Compile data to describe benchmark building, including:
  Physical properties (building envelope and thermal properties)
  Space conditioning system
  Initial assumptions for internal loads and building operations (to be calibrated in Step 2)
= initial benchmark building model = simulation input file

## Slide 11: Step 2: Pre-Implementation Calibration
Procedure:
  Run simulation using input file from Step 1
  Compare simulation output for the benchmark building to data typical for the building stock or new construction
  Iteratively refine modeling rules (assumptions on internal loads and building operation), as needed
Result: Calibrated version of eQUEST = pre-defined set of modeling rules
Notes: ASHRAE Guideline 14-2002 or the IPMVP
<number>

## Slide 12: Step 3: Computer Simulation to Estimate Energy Savings
Energy savings for baseline and project building are simulated using project building input file:
  ex ante (for validation purposes)
  ex post (for crediting purposes), using actual weather data and emission factors for the year in question
Baseline & project models are identical, except for the mitigation measures (all other factors, including weather and occupancy, are uniform)
Isolation of effects of mitigation measures is major advantage of simulation approach

## Slide 13: Step 4: Monitoring
Pre-Validation Information
Software Version
Step 1 input files to define benchmark building
Step 2 information documenting calibration process
Step 3 input files for project building
During Crediting Period
Weather data
Electricity emission factor (if applicable)
Input and output files from model simulation of electrical and thermal energy savings performed under Step 3
Energy consumption of the project building on at least a monthly basis

## Slide 14: Step 4: Optional Post-Installation Calibration
Deviations in energy use obtained from post-installation monitoring (e.g., utility bills) compared with simulated output values
When measured data for project building are:
    ≤ simulated value: Use simulated energy consumption in baseline and project activity
    < 20% higher than simulated value: Use simulated energy uses in baseline and measured data for project activity
    > 20% higher than simulated value: PP may either: (i) apply simulated energy uses in baseline and measured data for the project activity to calculate energy savings and emissions reductions, or (ii) re‐calibrate the model to the measured data and re‐apply the above approach.

## Slide 15: Step 5: Calculate ER
Emissions reductions from electricity
Emissions reductions from thermal energy
j = reference building type
ES = modeled energy savings