## Slide 1: Session 2: The CDM project cycle Monitoring, Verification and CER issuance
SDM programme
UNFCCC secretariat
Training-Workshop to support the
“Uganda Municipal Waste Compost Programme”
21st -24th Oct 2013, Mukono Municipality, Uganda
Notes: Presentation title

## Slide 2: Outline
<number>
Monitoring
Verification
CER Issuance
Notes: Presentation title
Presentation title
The requirements on demosntration of additionality and deveolpment of EC for PoAs are set in the integrated PoA Standard, ‘Demonstration of additionality, development of eligibuility criteria and application of multiple meths for PoAs.‘
In this ppt we will focus only in the Additionality and EC part of the stnd.

## Slide 3: CDM Project Cycle
Monitoring report (MR) &
Request for issuance
Verified/certified MR &
Request for issuance
Project design
National approval
Validation
Registration
Verification / certification
Issuance of Certified Emission Reductions (CERs)
Monitoring
DOE
CDM EB
Project participant
Step
Who’s responsible
Notes: Presentation title

## Slide 4: 1. Monitoring
PDD
Registered
Verification by DOE of MP1
Monitoring Period 1 (MP1)
Monitoring Period 2 (MP2)
MP3
MP4, etc
Monitoring Report of MP1
DOE
UNFCCC
CERs
Monitored by PP based on:
- Monitoring Plan of PDD
- applied methodology
- current EB guidance
-Verification and Certification Reports
-Final Monitoring Report
-Other relevant documents
-Request for Issuance of MP1
Notes: Presentation title

## Slide 5
WHO?
The monitoring report form (CDM-MR) is intended to be completed by project participants.
WHY?
To present information related to the monitoring of the project activity during a monitoring period, and to support the DOE during the verification process.
WHAT?
Quantitative information such as reported numbers relating to the calculation of emission reductions achieved during the monitoring period.
Qualitative information such as implementation and operational status, internal controls, procedures for calculations and data transfer, collection and recording.
1. Monitoring Report Form
Notes: Presentation title

## Slide 6: Monitoring Report Form (CDM-MR)
The CDM-MR includes Guidelines1 to assist project participants in the completion of the form and contains the following sections:
  Description of the project activity;
  Implementation of the project activity;
  Description of the monitoring system;
  Data and parameters included in the monitoring plan;
  Emission reduction calculation
  1 http://cdm.unfccc.int/Reference/Guidclarif/iss/iss_guid07.pdf
Notes: Presentation title

## Slide 7: Monitoring Report Form (CDM-MR)
A) Description of the project activity;
Brief summary of the project activity:
  purpose of the project activity, installed technology;
  total emission achieved in the monitoring period;
  general information such as:
    project participants
    location of the project
    methodology used and related guidelines
    crediting period
Notes: Presentation title

## Slide 8: Monitoring Report Form (CDM-MR)
B) IMPLEMENTATION OF THE PROJECT ACTIVITY
Detailed description of the implementation and operation of the project activity during the monitoring period.
Information with respect to unexpected changes against the PDD and the monitoring plan
C) DESCRIPTION OF THE MONITORING SYSTEM
Explanation of data collection procedures, organizational structure, roles and responsibilities.
Inclusion of line diagrams to:
    clearly show all relevant monitoring points;
    improve the transparency of the monitoring; and
    facilitate the future assessment done by DOE during verification.
Notes: Presentation title

## Slide 9: Monitoring Report Form (CDM-MR)
D) DATA AND PARAMETERS INCLUDED IN THE MONITORING PLAN
Include all parameters requested by the applied methodology
Parameters fixed ex-ante
Parameters to be monitored
Notes: Presentation title

## Slide 10: Monitoring Report Form (CDM-MR)
E) EMISSION REDUCTION CALCULATION
Provide the formulae used to calculate the final emission reductions including:
    baseline emissions;
    project emission; and
    leakage.
…using actual values obtained during the monitoring period.
Include a comparison of actual values of the emission reductions achieved during the monitoring period with the estimations in the PDD.
Notes: Presentation title

## Slide 11: 2. Verification
PDD
Registered
Verification by DOE of MP1
Monitoring Period 1 (MP1)
Monitoring Period 2 (MP2)
MP3
MP4, etc
Monitoring Report of MP1
DOE
UNFCCC
CERs
Monitored by PP based on:
- Monitoring Plan of PDD
- applied methodology
- current EB guidance
-Verification and Certification Reports
-Final Monitoring Report
-Other relevant documents
-Request for Issuance of MP1
Notes: Presentation title

## Slide 12: 2. Verification
Designated operational entity (DOE) verifies that emission reductions took place, in the amount claimed, according to approved monitoring plan.
<number>
Years
GHG emissions (tCO2eq)
Project implementation
Emissions baseline
Emissions after the project
Beginning of monitoring period
Verification / Certification of emission reductions
ADDITIONAL EMISSION REDUCTIONS
Notes: Verification is the independent review and ex post determination by the designated operational entity (DOE) of the monitored reductions in anthropogenic emissions by sources of greenhouse gases that have occurred as a result of a registered CDM project activity during the verification period.
Presentation title

## Slide 13: 2. Verification
Essentially, seeks to confirm two things:
  – that past greenhouse gas performance has been appropriately calculated and reported
  – that the project has been executed in accordance with the validated PDD
Verification is undertaken by a DOE
  – For projects applying large scale methodology, different DOE other than the one performing the validation;
  – For projects applying small scale methodology, same DOE can performing both the validation and verification.
  – There are forty two DOE had been accredited as of today.
Verification can take place as often as the project developer wishes – represents a balance between cost and revenue
<number>
Notes: Presentation title

## Slide 14: Verification approach/requirements
Involves the review of documentation and on-site visit (s), and is based on quantitative and qualitative information.
Documentation includes:
  monitoring documentation;
  registered PDD;
  validation report;
  previous verification reports;
  applied methodology;
  relevant decisions / clarifications / guidance from the CMP and the CDM Executive Board;
  any other relevant information or reference (e.g. external data).

## Slide 15: Verification outcomes
a) Verification Report, among others providing:
summary of the verification process and the scope;
findings of the desk review and site visit;
findings and conclusions as to implementation of the project, against PDD, compliance with monitoring plan, assessment of data and calculation;
list of each parameter specified by the monitoring plan and how it is verified;
conclusion on the verified amount of emission reductions achieved.

## Slide 16: Verification Outcomes
b) Certification Report
“Certification is the written assurance by the DOE that, during a specified time period, a proposed CDM project activity achieved/resulted in the emissions reductions as verified.”
The certification report must include:
monitoring period under verification;
emission reductions certified by the DOE.

## Slide 17: What you need to know about verification…
The best project in the world is worthless if not monitored properly:
If the project developer does not collect, process and record relevant data during the operation of the project, it is usually not possible to reconstruct (back-cast) this data;
If data is not transparently available to the DOE, certification will not be possible;
If the Monitoring Report fails verification, the project cannot be issued with CERs

## Slide 18: 3. Issuance
PDD
Registered
Verification by DOE of MP1
Monitoring Period 1 (MP1)
Monitoring Period 2 (MP2)
MP3
MP4, etc
Monitoring Report of MP1
DOE
UNFCCC
CERs
Monitored by PP based on:
- Monitoring Plan of PDD
- applied methodology
- current EB guidance
-Verification and Certification Reports
-Final Monitoring Report
-Other relevant documents
-Request for Issuance of MP1
Notes: Presentation title

## Slide 19: 3. CER issuance
The DOE provides a verification report and certification report to the project participants and the executive board.
• Verification report once received by the secretariat, will undergo
  The Completeness check;
  Vetting by secretariat
  vetting by Executive Board
If a Party or three members of EB request review, issuance request undergoes review, otherwise proceeds to issuance
If a review is requested the CDM Executive Board may reject the request
<number>
Notes: Presentation title

## Slide 20: THANK YOU!
UNFCCC secretariat, SDM programme
Notes: Presentation title

## Slide 21: The link between validation and verification
Before the project…
Validation gives assurance that if the project is implemented according to the Project Design Document (PDD) then it will meet CDM eligibility criteria and that, once verified, CERs will be issued.
During the project…
Verification provides assurance that the project developer has adhered to the validated PDD and that emission reductions have, in fact, taken place.