## Slide 1: Bulgaria GHG Emission Projections - Results and Methodological Problems Dr. Christo Christov Energy Institute JSCo Sofia, Bulgaria
Bonn, Germany
6-8 September 2004

## Slide 2
Energy Institute is an independent private joint-stock company dedicated to providing solutions in the field of energy, environmental protection and climate change.
For the recent two years we have developed more than 100 projects in the field of the nuclear and thermal energy, power transmission and distribution, co-generation, district heating and renewable energy.
Energy Institute and climate change:
The First, Second and Third National Communications on Climate Change,
National Greenhouse Gases (GHG) Inventories and National Inventory Reports for the years 1988, 1990 – 2002.
Advises to the Governmental officials on national policies and measures for reducing GHG emissions
The National Action Plan on Climate Change approved by the Bulgarian Government in 2000

## Slide 3: BULGARIA and UNFCCC
Bulgaria ratified the Convention in March 1995, thus committing to keep its GHG emissions below those in the base year.
Pursuant to article 4 (section 2c and 6) of the UNFCCC, Bulgaria used its right to choose as a base year different from the commonly accepted 1990, i.e. 1988.
Bulgaria ratified the Kyoto Protocol to the UNFCCC on August 15th, 2002. The target adopted by Bulgaria is an 8% reduction compared to the base year 1988.

## Slide 4: Historic overview of GHG emissions

## Slide 5: Summary
In 2002 Bulgaria has achieved 79 million ton GHG emission reduction (minus 56%) compared to the base year 1988.
The main reduction drivers:
Governmental policies for transition to the market economy, restructuring of industry, privatisation and liberalization;
Energy policy towards liberalization of the energy market and removal of subsidies;
The GHG intensity (GHG/GDP) of the Bulgarian economy decreased by 46% from 3.63 kg CO2 eq./ BGN(2002) in 1988 to 1.95 kg CO2 eq. / BGN(2002) in 2002.
The accounted emission reduction of 79 million ton results from two factors:
GDP and population decrease: 26 million ton (33%);
Economic and energy policies: 53 million ton (67%).

## Slide 6: GHG Emission Forecast
The GHG emission forecast is based on projections for the following indicators:
Demographic development;
GDP development of sectors and sub-sectors;
Change in the energy-intensity of the industries and services as a result of improved energy efficiency / production technologies;
Changes in the energy-intensity of households as a result of the development of income and improved energy-efficiency of dwellings and appliances.

## Slide 7
For the demographic development official projections of the Government are used –
the population size will further decline with 0.8% per year in the period 2003-2009,
followed by an annual reduction of 0.6% in the period 2010-2020.
As a result, it is projected that in 2020 the country population will reach 6.9 million people.
The GDP forecast assumes a
5.25% growth for 2004-2005 and
5.5% for the 2006-2016 period.
After then, the growth gradually declines to 3.5% in 2020..
The forecast of total GHG emissions are based on the cumulative forecast for each sector.

## Slide 9: Methodology
Within the last years there was no place for the capacity building activities in the field of GHG emission projections.
The methodology and approach that were adopted during the US CSP are still applying.
Macroeconomic forecasts – Governmental agencies
Demographic Forecast;
GDP forecast by sectors and sub-sectors (following IPCC Inventory sectors): Metallurgy, Chemical Industry, Construction materials, Other industries, Agriculture and forestry, Transportation, Services.

## Slide 10
Activities forecast – independent experts
Final energy demand forecast by energy and fuel types and by sectors
Production volumes forecast by sectors
Energy sector construction plan (heat, electricity, oil and oil products, coal, gas)
Primary energy demand forecast
Waste sector plans

## Slide 11: GHG Emission forecast
Following the IPCC classification of the sectors:
Energy and sub-sectors
Industrial processes
Agriculture
Waste
The information Data base for the parameter and emission factors according to the IPCC methodology that is applied for the annual inventories in the country is used

## Slide 12: GHG Emission forecast follows the Inventory methodology:
Energy by sub-sectors
ENPEP package for integrated energy planning
The information Data base for the fuel and technology aggregation and emission factors that is applied for the annual inventories
Industrial processes, Agriculture and Waste sectors by sub-sectors
Spread sheets and the information Data base for the sub-sectors parameter and emission factors that is applied for the annual inventories. The mitigation measures and technological changes are reflected in the sub-sectors emission factors change

## Slide 13: Problems
The privatization of the industry and services is almost entirely finalized and
the state experts from the relevant ministries are not already concerned with the reporting, control and planning of the sectoral activities and
they are not in the capacity of giving forecasts for the development of the industry and services.
This situation considerably makes difficult the work of the team of the Energy Institute which elaborates the projections for GHG emissions.
In the forecasts elasticity of the production volume and energy demand to the GDP and population is applied

## Slide 14: Needs
Considerable improvement of the capacity in all ministries and creation of units for projection of the development of the economic sectors.
Significant improvement of the capacity for development and assessment of the effects of the policies and measures
Further improvement of the capacities of the Ministries to select and assess the political instruments that would make the measures happen
Transportation models for activities forecast and for emissions forecasts
Agricultural models for activities forecast and for emissions forecasts

## Slide 15: Contacts:
Dr. Christo Christov,
Executive Director
Energy Institute, 20 Joliot – Curie Str.,
Sofia 1113, Bulgaria
Phone: (359 2) 969 86 38, Fax (359 2) 963 40 38,
GSM (359 88) 82 83 889
E-mail: christov@eninbg.com; office@eninbg.com