## Slide 1: The ECN model structure for energy projections
Ton van Dril
ECN Policy Studies
vandril@ecn.nl
UNFCCC Workshop on Emissions Projections
Bonn 6-8 september 2004

## Slide 2: Modeling specific developments in energy consumption on the technology level ( ottom-up)
B

## Slide 3: The technological bypass
Statististics:
Energy
Physical data
Value added
General sectoral characteristics,
Production capacity
Proces and technology data
Reconstruction of
energyfunctions,
and technology
Outlook for energy functions and technology penetration
Expectations on
Energy functions and
technologies
Expectations on economic, structural and policy developments
Outlook for energy,
Physical production
Value added
Model
system

## Slide 5: Demand model inputs
Sectoral economic inputs:
  CPB Athena or macro data > ECN sector model
Energy prices: - world markets for fuels, CO2
  feedback from supply model for electricity
Physical capacity and material flows: -ECN process capacity data, Stream model on 5 major physical substances
Technologies: -Households gas and power use surveys, UU Icarus4 database, buildings and horticulture data (ECN, LEI)
Implementation characteristics: -Expert judgements
Policies: -policy model

## Slide 6: Supply model inputs
Existing capacity, installation level
Fuel prices
CO2 price and CO2 costs pass-through
Operational characteristics, mark-ups and liberalisation/market power, cross-border supply characteristics, etc.

## Slide 7: Technology implementation characteristics

## Slide 8: Technology implementation characteristics
0%
20%
40%
60%
80%
100%
120%
1
3
5
7
9
11
13
15
17
19
21
23
implementation
period
1/Lplant
1/Lold
Lold: Lifetime of the old equipment
Lplant: Lifetime of the equipment surroundings
2
Capital
replacement
limitations

## Slide 9: Technology implementation characteristics

## Slide 10: Options penetration process, year t
Evaluation of IRR, competing options
Potential options shares
Total capacity increase +
Replacement of reference technology +
Replacement of older options
(lifetime not influenced by taxes, etc)
Available capacity for options
Limitations for separate options
Max capacity per option
Options division, year t

## Slide 11: Policy model step 1
policy makers have to identify:
  desired physical changes
  decision makers and their scope
  occurences of decision

## Slide 12: Policy model step 2
policies have to create:
  attention (awareness)
  possibilities (technical, legal)
  advantage (financial, avoid sanctions)
>>effective policies meet all three conditions

## Slide 13: Policy model step 3
attention policies: information campaigns, building regulations, environmental permits, covenants
  >often taken for granted
possibility policies: R&D, demonstration, audits, company plans
  >options, replacement rate and implementation characteristics
advantage policies: taxes, subsidies, regulation and sanctions, emission markets
  >IRR evaluation

## Slide 14: Strenghts and weaknesses
Looking ahead for new trends or limitations
Limited data set of options requires filling the blanks
No feedback of energy costs on sector growth
Data requirements and validation
Awareness and information costs

## Slide 15: Further ideas for improvement
Multi layer approach: select processes first, then energy options, then short term behavior, then on-site supply options
Demand sector growth depending on climate policies: emissions trading
Awareness and information costs
Multi criteria + limited options

## Slide 16: Further ideas for improvement
Consistency in energy and CO2 prices
Consistency in international economic developments
Consistency of improvements on global technologies
Consistency in EU policy perspectives
Consistency in uncertainties regarding the previous bullits

## Slide 17: Research suggestions
Projection comparisons using the demonstrated methods
Divide tasks among research groups/countries
Analyse and compare policy impacts

## Slide 18
2. Transport
1. Duurzaam
6. SERUM
10. SELPE
8. SAVE-Industry CHP
7. SAVE-services
5. SAVE-HH
4. Tarieven
9. Powers
11. Monit, PIE
conversie
Tabellen
set
MONIT
RIVM
3. Gaswinning
Excel
dataconversie
GAMS
AIMMS
Excel/Vensim
AIMMS
dataconversie
Excel
Excel/GAMS
12. SpecialFuels