## Slide 2: United Nations Framework Convention on Climate Change Workshop on Emission Projection Issues in the Preparation of GHG Projections for the Energy Sector, Transport, Industry and Waste Management in the Czech Republic Bonn, Germany, 6 - 8 September 2004
Mr. Jiří Spitz
ENVIROS, s. r. o., Prague, Czech Republic
Phone: +420 284 007 486
Fax: +420 284 861 245
E-mail: jiri.spitz@enviros.cz
www.enviros.cz

## Slide 3: Breakdown of GHG emissions - 1

## Slide 4: Breakdown of GHG emissions - 2
Total emissions of greenhouse gases in 2000 were 143 665 and in 2001 143 692 thousands tons CO2ekv.
The greatest share in GHG emission has CO2 (86,2 %) and 99,6 % of it is produced in combustion processes. The further breakdown of it is:
  energy sector - 48,4 %,
  industry (including industrial heat and electricity) - 29,0 %,
  households, agriculture and tertiary sector - 13,7 %,
  transport - 8,9 %.

## Slide 5: Breakdown of GHG emissions - 3

## Slide 6: Breakdown of GHG emissions - 4

## Slide 7: Key GHG sources
CO2
  energy sector - 48.4 %
  industry - 29 %
CH4
  fugitive emissions from fuels - 52.5 %
  agriculture - 22.3 %
  waste management - 20.3 %
N2O
  agriculture - 63 %
  chemical industry - 13.8 %
  energy industry - 8.2 %
  transport - 6.3 %

## Slide 8: Modelling tools - 1
Basic tool used for GHG projections in energy, transport, industry and waste management sectors is EFOM/ENV model. It is a linear optimising and technology-oriented model.
It covers the following sectors:
  power sector
  district heating
  agriculture
  households
  tertiary sector
  transport
  industry
  industrial co-generation
  gas sector
  oil sector
  coal sector

## Slide 9: Modelling tools - 2
The model directly calculates the following emissions:
  CO2
  SO2
  NOX
  CO
  CH4
  solid particles
The covered emission sources are:
  combustion processes in all sectors
  fugitive emissions from mining, transport and processing of coal
  fugitive emissions from mining, transport and processing of natural gas
  emissions from ferrous metallurgy

## Slide 10: Modelling tools - 3
Topics uncovered by the used version of EFOM/ENV model
  N2O emissions
    calculated using simple spreadsheet model by sectors
  HFCs, PFCs, SF6 emissions
    calculated using simple spreadsheet model on the national level only
  industry processes other than ferrous metallurgy
    projection was made for cement production and glass industry using emission coefficient calculated by the IPPC methodology
  emissions from waste management
    calculated using simple spreadsheet model

## Slide 11: Modelling tools - 4
Energy demand is calculated by sectors and types of energy use using spreadsheet model based on similar principles like MEDEE model (GDP & population trends, trends in energy intensities and efficiencies etc.).

## Slide 12: Mitigation measures - 1
Besides the technology improvements, fuel switch, savings etc. calculated by the model there were measures not covered by the model. These are mainly:
  programmes of the Czech Energy Agency,
  programmes of the State Environmental Fund.
Both Czech Energy Agency and State Environmental Fund produce annual reports containing besides other emission reduction caused by realised actions. GHG projections were made from relation between budget and reached emission reduction. Of course, there are many assumptions, because it is difficult to estimate emission reduction from such actions like energy consulting, energy audits or regional energy concepts.

## Slide 13: Mitigation measures - 2
Since it is possible to set up price for any energy carrier in the model, the model reflects:
  different taxation of various fuels
  feed-in tariffs for electricity produced from renewable energy
  feed-in tariffs for electricity from small co-generation
The energy tax is one of the most uncertain topics in the CR. The Ministry of Environment prepares very ambitious energy tax reform, whereas the Ministry for Industry and Trade requires introduce the lowest possible energy tax given by the EU directive. In the recently approved “State energy concept” the view of Ministry of Industry and Trade was accepted.

## Slide 14: Emission trading
Realised and planned jointly implemented actions were taken into account.
No other kind of emission trading was taken into account.

## Slide 15: Thank for your attention!
Contacts:
ENVIROS, s. r. o.
Prague, Czech Republic
Phone: +420 284 007 499
Fax: +420 284 861 245
E-mail: office@enviros.cz
www.enviros.cz