## Slide 1: US Approach for Projected Greenhouse Gas Emissions
Casey Delhotal
Issues in the preparation of GHG projections for the energy, transport, industry and waste management sectors
UNFCCC Workshop on Emissions Projections
Bonn, Germany Sept6-8, 2004

## Slide 2: Overview of Projections Methodology
CO2 emissions from energy, transportation and industry calculated using the National Energy Modeling System (NEMS) model.
Non-CO2 emissions calculated separately.
Policies and measures in place as of July 1, 2001 modeled in baselines; future, potential policies not modeled.

## Slide 3
http://www.eia.doe.gov/oiaf/aeo/overview/overview.html
National Energy Modeling Systems (NEMS)
Notes:   Coverage: CO2 from
    residential
    industrial
    commercial
    transportation (also N2O)

## Slide 4: Assumptions Used in NEMS

## Slide 5: Assumptions Used in NEMS

## Slide 6: Policy Coverage in NEMS
Impacts and costs of legislation and regulations adopted as of July 1, 2001, including:
    appliance and lighting efficiencies (Energy Star specifications)
    adoption of electric and alternative-fuel vehicles in accord with federal and state requirements.
    renewable fuel requirements, etc.
Impact of the President’s climate change initiative and the National Energy Policy NOT included in analysis.

## Slide 7: Methane from Coal Mines
Projected coal production x basin specific emission factor = emissions
Driver: coal production projections from NEMS/American Energy Outlook (AEO)
Projected reductions from voluntary program/EPAct Reductions subtracted from projections

## Slide 8: Methane from Natural Gas Operations
Driver: NEMS natural gas projections for production, processing, and transmission & distribution
ICF Inc.’s Natural Gas model
  builds infrastructure to meet projected NG demand
  emissions associated with fugitives and venting related to equipment used in the infrastructure
Projected reductions from voluntary program subtracted from projections

## Slide 9: Methane from Landfills
Driver: projected population and estimates of recycling and waste diverted
Landfill model
  opening and closing of landfills to meet predicted waste disposal needs
  emissions calculated using linear decay
Projected voluntary reductions/reductions due to Landfill Rule (VOC reductions) subtracted from projected baseline

## Slide 10: HFCs, PFCs, and SF6 from Industry
Activity x Emission Factor = Emissions (IPCC Good Practice Guidance)
Calculated by industrial usage (ex: emissions for the semiconductor industry)
Drivers or activity = industrial production
Checked Against Chemical Sales Data (e.g., gas sales from AFEAS, RAND SF6 survey)

## Slide 11: ODS Substitutes
Detailed Yearly Market Data on Over 40 End-Uses
  Car ACs, Retail Food, Appliance Foam …
Track Market as it Transitions from ODSs into HFCs and Other Options
Emissions from Leaks, Service, Disposal
Incorporate Technology Improvements

## Slide 12: Vintaging Model Emission Profiles
Ref&AC: leaks from use, servicing, disposal
  Q is quantity of HFCs added in a given year
Fire Extinguishing: leaks/releases each year
Foams: manufacturing, use, disposal
Aerosols/MDIs: immediate emissions
Solvents: percentage leaked during first year (rest is recycled or disposed)

## Slide 13: Policies and Measures for HFCs, PFCs and SF6
Significant New Alternatives Program
  HFCs and PFCs associated with ODS substitutes
HFC-23 Partnership
Partnership with Aluminum Producers
Environmental Stewardship Initiative
  HFCs, PFCs and SF6 from semiconductor production, electric power systems, and magnesium production

## Slide 14: Nitrous Oxide from Adipic and Nitric Acid Production
Drivers
    adipic = projections of nylon consumption
    nitric = projections of fertilizers, explosives and adipic acid consumption
Reductions
    adipic acid plants reduce emissions by 95 to 98 percent through installed abatement technologies
    nitric acid plants reduce emissions through Non-Selective Catalytic Reduction NOx control (98%). Only at selected plants.

## Slide 15: Uncertainties Affecting Projections
Technology Development
Regulatory or Statutory Changes
Energy Price Changes
Economic Growth
Weather