## Slide 1: EXPERIENCE IN BELGIUM : ENERGY DEMAND MODELLING WITH THE EPM BOTTOM-UP MODEL
UNFCCC Workshop on GHG Emission Projections
Bonn, 6-8 September 2004
Francis ALTDORFER, ECONOTEC

## Slide 2
EPM (Emission Projection Model) :
Developed by ECONOTEC in the framework of studies for Belgian public authorities.
Has been used for the 3rd National Communication, in conjunction with the HERMES macroeconomic model (of the Federal Planning Bureau).

## Slide 3: METHODOLOGICAL APPROACH SOME KEY ISSUES

## Slide 4: Observation No. 1
In Belgium, a crucial role is to be played by energy demand management.
A large share of electricity production is covered by nuclear energy (56% in 2002) and natural gas (23%), while the potential for renewable electricity production is small.
Therefore the options for GHG emission reduction in the energy transformation sector are limited.

## Slide 5: Observation No. 2
There is no simple relationship between the economic activity of a sector and its emission level.
Importance of structural effects :
Within a same sector (iron & steel, non metallic minerals…), the intensity of CO2 emissions may easily vary by a factor of 10.

## Slide 7: Observation No. 3
There is a substantial emission reduction potential with negative costs.
This is confirmed by over 50 audits carried out by ECONOTEC on large industrial sites in all kinds of sectors.

## Slide 9: Methodological consequences
Need to be as as close as possible to the physical reality : a (very) disaggregated bottom-up type of model, activity variables in physical units.
Simulation rather than optimisation …
rather a sensitivity analysis to a set of hypotheses than a representation of the optimal solution.
Need to focus on energy demand modelling.

## Slide 10: MAIN FEATURES OF EPM

## Slide 11
EPM is a simulation model allowing to calculate :
- business-as-usual scenarios (unchanged policy);
- technical and economic potentials for reducing emissions;
- emission reduction cost curves and to simulate emission reduction scenarios.

## Slide 12
Essential characteristic of the model :
  the high disaggregation level of emission sources.

## Slide 13
Objectives of the disaggregation
  take into account structural effects within the sectors
  to better take into account the available field information (on plant closures, new investments…);
  to take into account mitigation measures specific to particular sources.

## Slide 14
Disaggregation levels
Industry
± 70 among the most energy intensive activities
iron & steel : 10 activities (sinter production, blast furnace, oxygen steel, hot rolling…)
chimie : ± 20 activities (ethylene, chlorine, vinyl chloride, ammonia…)
…

## Slide 15
Residential
Specific module for calculating the heat load of buildings :
  14 representative model-dwellings, with dimensioning and thermal characteristics;
  performance de 15 heat production, distribution and emission systems;
  sanitary hot water;
  10 specific electricity usages (cooking, refrigerators, washing machines, dryers…).

## Slide 16
Tertiary sector
30 sub-sectors, grouped in 8 categories :
  commerce
  banks, insurance…
  education
  health services
  public administrations
  culture, sports & leasure
  …

## Slide 17
Transport
Specific module for the detailed modelling of road transport :
  - 11 categories of vehicles
  - 3 types of driving patterns
  - 3 types de fuel
  - distribution of cars by age class
  - emission levels of the regulation in force when first put on the road

## Slide 18
Emission reduction potential
Technical potential: maximum penetration of each mitigation measure
Economic potential = fraction of technical potential for which :
  Marginal cost < Marginal cost ceiling

## Slide 19
The dispersion in costs from one site to another is taken into account.
Probability law around the mean value.
==> Avoids an “all-or-nothing” effect on the penetration of measures.

## Slide 20
Techno-economic database
on mitigation measures
Base year :
- detailed energy balance
activity variables
emission factors
…
Evolution of :
- activity levels
specific energy consumptions
fuel market shares
- emission factors
Business-as-usual scenario (BAU)
Emission reduction scenario
Scenario hypotheses :
- energy prices
ceiling on marginal reduction cost
discount rates
…
EPM scenario development

## Slide 21
Other features
  multi-pollutant (CO2, CH4, N2O, HFCs, PFCs, SF6, SO2, NOx, VOCs)
  modelling at regional and national level with same approach and common or harmonized hypotheses (has been applied for : Belgium, Wallonia, region of Brussels-Capital, Luxembourg)
        ./...

## Slide 22
possibility to calculate the impact on the reduction potential of measures such as :
    taxes, subsidies
    regulations
    efficiency improvement objectives (e.g. voluntary agreements)
easy updating in case of a modification of key variables (industry sector evolution, technological evolution…)

## Slide 23
  many exogenous data needed
  ==> large database, with permanent improvement process;
  allows to test the sensitivity to numerous parameters
  for macroeconomic framework, coupling made with macroeconomic model (HERMES in case of 3rd National Communication)

## Slide 24
New developments
Organisation of the transfer of the model to the administration of the Walloon Region (to allow it to make simulations by itself)
Coupling to GreenMod, macroeconomic general equilibrium model of the University of Brussels (Prof. Bayar)

## Slide 25: SOME CHALLENGES FOR GHG EMISSION MODELLING

## Slide 26
Size of the reduction potential with negative cost
Barriers to "rational decision making".
This makes it more difficult to assess the impact of policies, in particular of economic instruments (taxation…).

## Slide 27
EPM quantifis potentials with negative costs.
Tentative solutions :
use higher discount rates, to reflect the short payback-times required by consumers
introduce adjustment costs
reduce the weight of energy costs in objective function
…

## Slide 28
Link between bottom-up and macroeconomic modelling
Both approaches are complementary.
The difficulty stems in particular from the different disaggregation levels.
As mentioned above, EPM has been linked with HERMES and GreenMod.

## Slide 29
Projections of HFCs, PFCs and SF6 emissions
The 3rd Belgian National Communication did not comprise such projections. This is a relatively new area.
Since then, ECONOTEC has carried out these projections for the Federal Department of the Environment.

## Slide 30
Difficulties faced for F-gases :
the number of gases and mixtures of gases involved
the variety of emission sources
the fact that emissions often arise from stocks of gases accumulated in equipment
the shortage of data on stocks, losses, etc.
A specific model development has been carried out.