## Slide 1: Variations on the methane CO2-equivalence
Olivier Boucher
Laboratoire de Météorologie Dynamique, CNRS / UPMC, Paris, France
UNFCCC Workshop on common metrics to calculate the CO2 equivalence of anthropogenic
greenhouse gas emissions by sources and removals by sinks in Bonn, Germany (3-4 April 2012)

## Slide 2
Outline
1. Rationale
2. Biogenic vs fossil methane
3. Revisiting the GDP: implications for the GWP
4. Time-evolving CO2-equivalence
5. What metric for what usage?
6. Conclusion

## Slide 3
Why methane?
1. Second largest GHG in terms of RF
2. Significant anthropogenic emissions from a variety of sectors (agriculture, landfill, coal mining, conventional natural gas exploitation, shale gas exploitation) with some opportunities for mitigation
3. Multi-gas abatement strategies mostly sensitive to the methane CO2-equivalence  other long-lived greenhouse gases have either too small RF (e.g. SF6 or NF3) or a pretty invariant CO2-equivalence (e.g. N2O) to really make a difference from a climate perspective.

## Slide 4
Methane factsheet
Atmospheric concentration =1800 ppbv = 1.8 ppmv
(versus 380 ppmv for carbon dioxide)
Radiative efficiency = 3.7 10-4 Wm-2ppbv-1
(versus 1.548 10-5 Wm-2ppbv-1 for carbon dioxide)
Radiative forcing = 0.48 Wm-2 in 2005
(versus 1.66 Wm-2 for carbon dioxide)
Lifetime ≈ 10 years
Perturbation lifetime ≈ 12 years
Indirect effects on stratospheric water vapour, ozone, CO2 and aerosols
Global Warming Potential (on a mass basis)
21 initially and also in Kyoto protocol
23 in IPCC TAR (2001)
25 in IPCC AR4 (2007)

## Slide 5: Methane cycle
CO2
CO2
CO2
CH4
CH4
Use a larger GWP for fossil methane of 27 (Boucher et al., ERL, 2009)
OR
Count fossil methane as CH4 and CO2 in inventories (Gillenwater, ESP, 2008)
Biogenic
methane
Fossil
methane

## Slide 6: Global Damage Potential (GDP)
Discount
term
Marginal damage caused
by a pulse emission
Cumulative
… revisiting Hammitt et al. (1996) and Kandlikar (1996)
What damage function?
exponent function
hockey-stick function
S-shaped (or sigmoid)

## Slide 7
GWP 100 years
25 / 27
GDP linear
100 years
28 / 30
GDP linear
100 years – 2%
42 / 44
GDP quadratic
Infinity – 2%
24 / 26
GDP cubic
infinity – 2%
14 / 16
GDP linear
infinity – 2%
37 / 39
GDP quadratic
100 years – 2 %
31 / 33
RF  T
Discounting
Linearquadratic
Linearquadratic
Linearcubic
Integration to 
Integration to 
Quadraticcubic
Climate metrics: from GWP to GDP

## Slide 8
GWP 100 years
25 / 27
GDP linear
100 years
28 / 30
GDP linear
100 years – 2%
42 / 44
GDP quadratic
Infinity – 2%
24 / 26
GDP cubic
infinity – 2%
14 / 16
GDP linear
infinity – 2%
37 / 39
GDP quadratic
100 years – 2 %
31 / 33
RF  T
Discounting
Linearquadratic
Linearquadratic
Linearcubic
Integration to 
Integration to 
Quadraticcubic
Climate metrics: from GWP to GDP

## Slide 9: Uncertainties in methane CO2-equivalence
Ozone
Water vapour
Methane lifetime
Oxidation fraction
CO2 RF
Climate
sensitivity
parameters
warming
Damage function
Discount rate
GDP

## Slide 10: Histogram of GWP and GDP

## Slide 11
GWP 100 years
25 / 27
GDP linear
100 years
28 / 30
GDP linear
100 years – 2%
42 / 44
GDP quadratic
Infinity – 2%
24 / 26
GDP cubic
infinity – 2%
14 / 16
GDP linear
infinity – 2%
37 / 39
GDP quadratic
100 years – 2 %
31 / 33
RF  T
Discounting
Linearquadratic
Linearquadratic
Linearcubic
Integration to 
Integration to 
Quadraticcubic
Climate metric: cumulative vs end-point
GTP end-point
100 years
4 / 6
End-point  cumulative

## Slide 12
Time-evolving CO2-equivalence
CO2-equivalence for
short-lived species tend to increase as climate change increases.

## Slide 13
Issue: CO2-equivalent emissions may go up even if individual gas emissions go down
CO2
CH4
CH4
CO2
CH4
CH4
2010
2020

## Slide 14
Solution: recalculate past emissions with new CO2-equivalence
CO2
CH4
CH4
CO2
CH4
CH4
2010
2020

## Slide 15
Estimate the total (i.e. CO2-equivalent) GHG emissions for countries and estimate time variations
Formulate emission targets at the international level
Break down emission targets between gases within individual countries
Trade emissions in emission trading scheme (ETS) or offset emissions through the Clean Development Mechanism (CDM)
Guide investment decisions across different gases
Should we use the same climate metric
for these different applications?
Multiple applications to climate metrics

## Slide 16
ADEME, France
Methane CO2-equivalence 100-year GWP=21
Source: Wikipedia

## Slide 17: Methane and the CDM
From Exec board annual report 2010, Clean Development Mechanism, UNFCCC
Emission reductions from CDM projects are monitored and credits are accrued year on year. Projects last for 10 years or 7 years with up to 2 renewals. Additionality does not have to be re-assessed.

## Slide 18
Multiple applications to climate metrics
Emission trading scheme / CDM
- pulse metric to calculate CO2-equivalence and trade
- 21 years is a long time for assuming additionality
Investment decision / CDM
- pulse metric
- visibility on future CO2-equivalence
- cost-benefit analysis (multi-year, discounting, …)
CO2 equivalent emissions
- pulse metric as long as on an emission trajectory
- sustained metric in stabilisation regime?

## Slide 19: Conclusions (1/2)
The 100-year GWP is comparable to an idealised GDP metric (with quadratic damage function and 2% discount rate).
An important discriminator for the methane CO2-equivalence among published climate metrics is whether the metric is cumulative or end-point (i.e. GTP vs iGTP / GWP / GDP).
For an idealised GDP, the methane CO2-equivalence is essentially determined by socio-economical parameters that involve a value judgment on impacts and discounting.

## Slide 20: Conclusions (2/2)
There is no reason for CO2-equivalence to stay constant, eg
GTP as we approach the target for an end-point metric
GDP as climate change unfolds with a convex damage function
 back-calculation of CO2-equivalent emissions
visibility on future evolution is required
Pulse emissions make sense for
- trading CH4 and CO2 on ETS and through the CDM
presenting a snapshot of a country emissions
It is less clear whether the same metric should be used to provide long-term stabilisation climate target.
 transition period

## Slide 21
Thank you for your attention Questions?