## Slide 1: Beyond the GWP: new interpretations and new metrics – a bit of a random walk …
Keith P Shine
Department of Meteorology, University of Reading
Particular thanks to Jan Fuglestvedt (CICERO) for so many metric conversations …

## Slide 2: Contents
Introductory remarks
The Global Warming Potential (GWP) – some issues which led to the GTP
The TEMP index – an “empirical” GWP
Two basket approach
Beyond global means …
Concluding remarks

## Slide 3: Contents
Introductory remarks
The Global Warming Potential (GWP) – some issues which led to the GTP
The TEMP index – an “empirical” GWP
Two basket approach
Beyond global means …
Concluding remarks

## Slide 4
What we are trying to do – a reminder
From Ozone Assessment “metrics” meeting, Boulder, November 1990 – Artists impression of slide, maybe presented by Bob Watson? Remembered by Dick Derwent

## Slide 5: Contents
Introductory remarks
The Global Warming Potential (GWP) – some issues which led to the GTP
The TEMP index – an “empirical” GWP
Two basket approach
Beyond global means …
Concluding remarks

## Slide 6: Global Warming Potential - the elephant that never forgets
Pulse emission at time t=0: Absolute Global Warming Potential (GWP) is the area under this curve to some given time
Other physical interpretations are possible! See other talks

## Slide 7: Kyoto – some questions
How did something that was “adopted ... to illustrate the difficulties inherent in the (metrics) concept” (to quote the IPCC WG1 FAR) become embedded in a major piece of international legislation?
Why has the IPCC (not solely IPCC WG1!) been so lax in considering alternatives?

## Slide 8: Shine’s theory of the inadvertent consensus
Policymakers are happy with the GWP
IPCC are happy with the GWP
IPCC
Policymakers
Shine 2009Climatic Change 96:467-472

## Slide 9: Choices for metrics
What parameter? e.g. radiative forcing, temperature change, sea-level rise, economic impacts, or the rate of change of these?
What emission? Pulse, sustained,…?
What time horizon?
Value at a given time or integrated over a given time horizon, and/or discounted?
The above choices affect decisions as to whether it is (perceived) best to cut short-lived or long-lived gases – and the choice of metric depends on the policy that it aims to fulfil!

## Slide 10: Are GWPs suitable if we have a target-based climate policy, such as the Copenhagen Accord?
Nature, 410, 675-677, 2001
NO!

## Slide 11: MERGE model
Manne and Richels, Nature, 2001
(see also Bradford N&V, Nature 2001)
“... Integrates sub-models … (with) … reduced-form description of energy sector, economy, emissions, concentrations and temperature change, disaggregated over space and time”

## Slide 12: Manne and Richels’ problems with GWPs
Failure to incorporate damage and abatement costs
Arbitrary choice of time horizon
Assumption that the metric values remain constant over time
Independent of the ultimate goal
“illogical” … “doesn’t make economic sense”

## Slide 13: Can a purely physical metric do a useful job?
Important to understand behaviour of climate parts of “integrated” models
Physical metrics may be more acceptable to policymaking community – fewer assumptions, more transparency
What is the simplest possible metric that can do this?

## Slide 14: Using the GTPP(t) to “mimic” Manne and Richels
λ = 0.8 K(Wm-2)-1
Shine et al. Phil Trans Roy Soc, 2007
Manne and Richels (2001)

## Slide 15: Impact on individual country “emissions” – GWP to GTP
Provisional data from Fraser and Shine
Change in CO2 equivalent emissions in going from GWP(100) to GTP (100) (an arbitrary choice of time horizon) – Kyoto Gases – uses GTP values from Fuglestvedt et al (Atmos. Env. 2010)

## Slide 16: Contents
Introductory remarks
The Global Warming Potential (GWP) – some issues which led to the GTP
The TEMP index – an “empirical” GWP
Two basket approach
Beyond global means …
Concluding remarks

## Slide 17: An alternative test of the GWP
Tanaka et al. (Climatic Change 2009)
Look at historical temperature changes due to CH4 and N2O emissions
How well are these temperature changes simulated if these emissions are replaced by their CO2-equivalent emissions using the GWP (any time horizon)?
And what is the best multiplier to achieve agreement? The TEMP index

## Slide 18: “Best” GWP and the TEMP index
Tanaka et al. Climatic Change, 2009
Reinforces the point that GWP(100) has a lack of temperature equivalence
The same calculation for N2O generates a TEMP that does not correspond to any GWP time horizon (the value is higher)

## Slide 19: Time-dependent “TEMP”
What happens if the best fit is over the period to some target year?
Maybe like the IGTP? Resembles the GTP(t) in shape
Tanaka et al. Climatic Change, 2009

## Slide 20: Contents
Introductory remarks
The Global Warming Potential (GWP) – some issues which led to the GTP
The TEMP index – an “empirical” GWP
Two basket approach
Beyond global means …
Concluding remarks

## Slide 21: A two-basket approach for a target-based policy
Steve Smith et al (to appear in Nature Climate Change)
2o target could be met by setting a cumulative emissions limit for long-lived gases and a maximum future rate of emission for short-lived gases.

## Slide 22: Gases naturally separate into two baskets
Shorter-lived gases: peak temperature change more related to sustained emission rate – absolute metric is like a sustained AGTP – (K (kg/yr)-1) … sustained GTP≈GWP
Longer-lived gases: peak temperature change more related to cumulative emissions – absolute metric is is in K kg-1
Smith et al. Nature Cli Change, 2012

## Slide 23: Two baskets – long-lived and short-lived
Gas | Lifetime (years) | Relative Peak Commitment T | GWP(100)
CO2 | - | 1 | 1
N2O | 114 | 309 | 298
CF4 | 50000 | 13900 | 7390
Gas | Lifetime (years) | Relative Sustained Emission T | GWP(100) (relative to CH4)
CH4 | 12 | 1 | 1
HFC134a | 14 | 47 | 57
HFC152a | 1.4 | 5 | 5
One conclusion may be that the GWP doesn’t do a bad job for both baskets – another reinterpretation? Early days …
Smith et al. Nature Cli Change, 2012

## Slide 24: Contents
Introductory remarks
The Global Warming Potential (GWP) – some issues which led to the GTP
The TEMP index – an “empirical” GWP
Two basket approach
Beyond global means …
Concluding remarks

## Slide 25
Metrics: often used for comparison of climate impacts of emissions from various sources, sectors or nations
Usually based on global-mean input
 important information on smaller scales may be lost
GWP
….
Beyond global means …
Lund et al. Climatic Change, 2012c
Notes: Metrics are of course a very useful tool for aggregating information and for comparison of climate impacts of emissions from various sources, sectors or nations.
Metrics are usually based on global-mean input such as global-mean temperature change or global warming potential, which means that important spatial variability is hidden and small scale informations may be lost. Even for relatively homogeneous changes in GHG concentrations, the climate response is quite inhomogeneous. Other atmospheric species, especially the short-lived produce distinctly heterogeneous RF which causes further inhomogeneity in the response.
<number>

## Slide 26
D = α(ΔT)n (e.g. Kandlikar (1995,1996), Hammitt et al. (1996)) – is the global-mean damage equal to the damage of the global-mean climate change?
Standard metric
Global-mean input
Alternative metric
”Local” input
How much information is lost when calculating the damage using global-mean input?
Here results from one (slab-ocean) climate model are presented, to illustrate the impact of ozone precursor emissions from the transport sector. An exploratory approach
Especially important when damage functions are used
Lund et al. Climatic Change, 2012
Notes: We use two simplified indicators, or metrics, to calculate the impact of the temperature change caused by OPE and aerosols from the transport sectors. Estimating the impact of climate change requires assumptions about the dependence of impact on the change. The basis for our definition of metrics is this impact (or damage) function, which has been used several times in the literature. In this the dependence on temperature change is often taken to be linear, quadratic or cubic and the definition is ofter applied at the global level using global mean temperature change as input.
  Following this we first define our standard metric, where the global impact is expressed as the square of the global mean temperature change. The impact can also be represented by a metric which includes more of the spatial heterogeneity in the temperature change. So we next define an alternative metric where any temperature change causes an impact. This metric is thus first calculated locally and then averaged globally, and our question is can we capture an additional signal by applying this metric?
We assume non-linear dependence of the climate impact on surface temperature change and using a quadratic relationship treats impact as symmetric, that is both positive and negative temperature change is equally harmfull. So I should highlight that our metrics are chosen mainly for illustrative purposes.
We define the heterogeneity ratio as the ratio of the alternative and the standard metric. A ratio higher than 1 means our alterntive metric captures a clearer signal of impact and the ratio is a measure of the heterogeneity in the temperature change.
Finally, we define a normalized heterogeneity ratio. This is the heterogeneity ratio of each transport sector to that of the more homogeneous CO2 concentration change, and it quantifies the excess of heterogeneity in the temperature change that can be directly attributed to the spatial distribution of the transport non-CO2 forcings.
<number>

## Slide 27
The global-mean “damage” is about 7 times greater than the “damage” calculated using the global-mean temperature change (and 6 times greater than that calculated for carbon dioxide changes)
Aviation NOx emissions as an (extreme?) example
Lund et al. Climatic Change, 2012
Notes: This figure shows annual mean surface air temperature change due to ozone precursor emissions from aviation and shipping in the ECHAM4 and Hadely center models. All panels show significant geographical variability. In the case of aviation, there is a significant inter-hemispheric difference. This is much less the case for shipping, and in fact the shipping pattern resembles that of the temperature change due to CO2.
<number>

## Slide 28: Contents
Introductory remarks
The Global Warming Potential (GWP) – some issues which led to the GTP
The TEMP index – an “empirical” GWP
Two basket approach
Beyond global means …
Concluding remarks

## Slide 29
There is nothing uniquely good about the GWP – it is an “accident of birth” that we use GWP(100)!
Nevertheless it enabled multi-gas climate policy; there would be costs in moving away from it.
And the GWP can be re-interpreted, in terms of physical meaning (iGTP, sustained GTP, …)
GTP? Maybe!
Incorporate economics? Maybe!
Move away from global means? Maybe!
Different formulations of multi-gas climate policy? Maybe!
Incorporate short-lived gases (CO, NOx)? Maybe, but …!
Some conclusions