## Slide 1: FIRST SDM JOINT COORDINATION WORKSHOP
24/03/2012 – 25/03/2012
Module 2.1 - Additionality

## Slide 2
First of its Kind (foik)
Common Practise (CP)
Challenges against the addiotionality demonstration.
Input to improve the current Approach of Additonality.

## Slide 3
First of Its Kind

## Slide 4: First of Its Kind
The project activity is the “first of its kind” if:
(a) For the measures identified under paragraph 6, a proposed project activity is the First-of-its-kind in the applicable geographical area if :
(i) The project is the first in the applicable geographical area that applies a technology that is different from any other technologies able to deliver the same output and that have started commercial operation before the start date of the project; and
(ii) A crediting period for the project activity that is “a maximum of 10 years with no option of renewal”;
(b) that was identified as the First-of-its-kind project activity is additional and Sub-step 3 b does not apply.
(c) For other measures Sub-step 3 b applies.

## Slide 5: Measures
Measure (for emission reduction activities) is a broad class of greenhouse gas emission reduction activities possessing common features. Four types of measures are currently covered in the framework:
(a) Fuel and feedstock switch;
(b) Switch of technology with or without change of energy source (including energy efficiency improvement as well as use of renewable energies);
(c) Methane destruction;
(d) Methane formation avoidance.3

## Slide 6: Different Technologies
Different technologies in the context of “first of its kind” are technologies that deliver the same output and differ by at least one of the following
(a) Energy source/fuel;
(b) Feed stock;
(c) Size of installation (power capacity):
(i) Micro
(ii) Small
(iii) Large.

## Slide 7
Common Practise

## Slide 8: Common Practise
Step 1: Calculate applicable output range as +/-50% of the design output or capacity of the proposed project activity.
Step 2: The proposed project activity and have started commercial operation before the start date of the project. Nall.
Registered and undergoing validation shall not be included in this step;
Step 3: Identify those that apply technologies different that the technology applied in the proposed project activity. Ndiff.
Step 4: Calculate factor F=1-Ndiff/Nall
Conclusion: PA is a ‘common practice’ if both the conditions are fulfilled:
(a) the factor F is greater than 0.2, and
(b) Nall-Ndiff is greater than 3.

## Slide 9: Different Technologies
Different technologies in the context of common practice are technologies that deliver the same output and differ by at least one of the following
(a) Energy source/fuel;
(b) Feed stock;
(c) Size of installation (power capacity):
(i) Micro
(ii) Small
(iii) Large;

## Slide 10: Different Technologies
(d) Investment climate in the date of the investment decision, inter alia:
(i) Access to technology;
(ii) Subsidies or other financial flows;
(iii) Promotional policies;
(iv) Legal regulations;
(e) Other features, inter alia:
(i) Unit cost of output (unit costs are considered different if they differ by at least 20 %);

## Slide 11
Challenges against the addiotionality demonstration

## Slide 12: Relevant national and sectoral policies
The Board agreed (EB 22 para 6) to differentiate the following two (2) types of national and/or sectoral policies that are to be taken into account when establishing baseline scenarios:
(a) National and/or sectoral policies or regulations that give comparative advantages to more emissions-intensive technologies or fuels over less emissions-intensive technologies or fuels; (E+)
(b) National and/or sectoral policies or regulations that give comparative advantages to less emissions-intensive technologies over more emissions-intensive technologies (e.g. public subsidies to promote the diffusion of renewable energy or to finance energy efficiency programs). (E-)

## Slide 13
Input to improve the current Approach of Additonality

## Slide 14: Input for Improvement
There should be some defined technology based on which project is Additional (eg. Landfill project with flaring of gas).
Reduce the efforts to demonstrate the additionality.
There can be the some predefine –ve & +ve list of technologies.

## Slide 15
Thank you for your attention!
Nikunj Agarwal